## Slide 1
On Ciphers that
Continuously Access
the Non-Volatile Key
Vasily Mikhalev, Frederik Armknecht, Christian Müller
University of Mannheim
March 07, 2017
Fast Software Encryption 2017, Tokyo, Japan

## Slide 2: Common Work Flow
Device
Non-volatile Memory
Key
Volatile memory, gates, etc..
Cipher
Load once

## Slide 3: New Work Flow
Device
Non-volatile Memory
Key
Volatile memory, gates, etc...
Cipher
Continuous
Access
Recent ciphers, e.g. KTANTAN and Sprout consider a different workflow

## Slide 4: Advantages of new Approach
Block Ciphers
  Avoiding using memory for key schedule => saving resources (Area, Power, Energy)
Stream Ciphers
  Secure stream ciphers with shorter internal state [FSE2015] => saving resources
  Higher level of security against certain attacks (e.g. TMDTO)

## Slide 5: Examples
Block Ciphers
  KTANTAN
  PRINTcipher
  LED
  Midori
  Other ciphers with precomputed key-schedule
Stream Ciphers
  A2U2
  Sprout
Notes: Put authors behind cipher names, e.g., Sprout (Armknecht, Mikahelev; 2015)

## Slide 6: Impact of the Approach
Papers consider approach of continioulsy accessing NVM as “free“
But how practical is this approach in the real life?
  NVM types and key management?
  Area size?
  Performance?
Notes: Add a section or slide on „Our contributions“.

## Slide 7: Our contributions
Feasibility of this Approach
Reconsideration of Existing Ciphers
Proposal of a New Cipher
New Building Block: Double-Layer LFSR

## Slide 8: Contribution 1: Feasibility

## Slide 9: NVM Categories and Key Management
Key has to be programmed by manufaturer, e.g. MROM
  Key has to be known before the device is produced 
  The approach to be cheap requires that a lot of devices share one key 
Key can be set only once, e.g. PROM
  Key has to be set before the device leaves the factory 
Key is rewritable, e.g. EEPROM, FLASH
  Flexible key management 

## Slide 10: Impact on Area Size
Irrespective of the memory type
  The key has to be read at least once in all ciphers
  The logic for this has to be implemented anyhow
  No big difference
  Some small extra area may be needed for synchronization

## Slide 11: Impact on Throughput
Key has to be programmed by manufaturer, e.g. MROM
    Instant access, no timing overhead 
Key can be set only once, e.g. PROM
  Instant access, no timing overhead 
Key is rewritable, e.g. EEPROM, FLASH
  Depends on the concrete type and on the way how the key needs to be accessed !
Memory categories

## Slide 12: Standard EEPROM
Common NVM in resource-constrained devices
Different technologies exist
  I2C
  Serial Peripheral Interface (SPI)
  Microwire
  UNI/O

## Slide 13: Reading Types
Selective reading
  Read from random address
  More flexibility
  Costly, lower throughput
Sequential reading
  Cyclically reading the next bit
  Less flexible
  Less costly, higher throughput
EEPROM
EEPROM

## Slide 14: Contribution 2: Reconsideration of Exiting Ciphers

## Slide 15: Standard EEPROM and Existing Ciphers

## Slide 16: EEPROMs Integrated into ASIC
In theory
  Almost no limitations and hence no influence on throughput
In real life
  Such EEPROMs are usually organized word-wise
  Word size directly influences the area size
  Typical word sizes for low area are 8, 16, or 32 bits
  Bit-by-bit approach can provide low power consumption

## Slide 17: ASIC EEPROM and Existing Ciphers

## Slide 18: Summary: Practicability
In general, the approach is practical
No big difference wrt the area size compared with standard approach
For non-rewritable keys (e.g. medical implants) no issues with timing
Otherwise ciphers risk to lose in throughput
Sequential processing of key bits (e.g. LED and Sprout) => almost maximal throughput irrespective of the memory type

## Slide 19: Contribution 3: New Design

## Slide 20: Problems of Sprout
2
7
7
f
LFSR (40 bits)
6
3
3
h
Round key function
g
NLFSR(40 bits)
29
…
…
Initialization phase
Initialization phase
Attacks
Notes: Mention again that this has been published by us at FSE 2015

## Slide 21: Sprout: Round Key Function
…
…
Counter
Select k(t mod 80)
Round t
LFSR
NLFSR
XOR
AND
L4
N9
N 20
N29
L37
L21
Notes: To do: Adapt text format (use same font as on other slides, etc.)

## Slide 22: Plantlet

## Slide 23: Implementation Results for Plantlet
UMC 0.18 process;
Clock frequency 100 kHz

## Slide 24: Planlet vs Other Ciphers

## Slide 25: Contribution 4: Double-Layer LFSR

## Slide 26: Double-Layer LFSR
Initialization
Keystream
generation
Uses primitive polynomials
LFSR of length 60
LFSR of length 61
Notes: Add some text on the benefits of this approach (no all zero state, maximum period, area, …)

## Slide 27: The end
Chart: 
| Thanks for your close attention | Thanks for your attention
 | 65 | 5
mikhalev@uni-mannheim.de